## Slide 1
Fig. 4: Magnitude of the SVD modes of the Hankel matrix. 7 modes were chosen to represent the lifted state.
Fig. 1: Bio-inspired soft grasper with contact sensing via pneumatic jaws [1]. The grasper decreases the enclosed area when moving from the rest state (A) to the actuated state (B). Without force control, the grasper can impart significant deformations (C).
Data-Driven Control of a Soft Bioinspired Grasper
Ravesh Sukhnandan1, Sreeram Thirupathi2, Helen Wang1, Nathan Zimmerer1
Carnegie Mellon University: 1) Mechanical Engineering, 2) Robotics Institute
Biohybrid and Organic Robotics Group
Introduction
Methods
Methods
Results
Results
Conclusions
Soft graspers have inherent advantages in handling fragile and deformable objects e.g. fruits, food, biological tissues
However, even very deformable items like soft clays may require active force control to minimize deformation
Fig. 3: Experimental setup to gather data for fitting using random step changes in controls on a fixed cylinder (N = 58).
Fig. 5: Koopman rollout vs real data. -> train and test.
Fig. 6: Simulation with PID for quasistatic and for Koopman. Add real hardware data with PID
Future Work
Fig. 2: Flow chart for controller development
A
B
C
Undeformed clay cube
After grasp
No force control
Observables:
Controls:
P1
P2
P3
x
y
x
y
. . .
x
y
Random step changes in controls
1
2
N
object
Soft graspers exhibit behaviors that are hard to analytically model e.g. non-linear material properties, hysteresis, deformable contact etc.
We use a data-driven approach to get the dynamics of the grasper so we can apply optimal control techniques.
Experimental Data
Fit dynamics
(MATLAB n4sid)
Design Controller:
LQR, PID
Test controller on hardware
Goal: Track arbitrary contact pressure trajectories during grasping of rigid and deformable objects using optimal control techniques
Try the LQR controller on hardware and compare the result to the simulation
Gather more data for the dynamics regression:
  Cylinders of different sizes
  Materials of different rigidity (PLA and soft clay)
Quantify deformation induced on deformable material with LQR controller and compare to existing neural-network open-loop controller [1]
NN open-loop
LQR
?
References
[1] R. Sukhnandan et al., LNCS, 2023
The system was simulated using both LQR and PID control strategies for the quasi-static case.
The performance of these controllers was evaluated in the context of time-delay embedding.
The results from the real hardware data were compared with the simulation results for both LQR and PID controllers.