## Slide 1
Fig. 4: Magnitude of the SVD modes of the Hankel matrix.
7 modes were chosen to represent the lifted state, .
Fig. 1: Bio-inspired soft grasper with contact sensing via pneumatic jaws [1]. The grasper decreases the enclosed area when moving from the rest state (A) to the actuated state (B). Without force control, the grasper can impart significant deformations on very soft plastically deformable objects (C).
Data-Driven Control of a Soft Bioinspired Grasper
Ravesh Sukhnandan1, Sreeram Thirupathi2, Helen Wang1, Nathan Zimmerer1
Carnegie Mellon University: 1) Mechanical Engineering, 2) Robotics Institute
Introduction
Methods
Methods
Results
Results
Soft graspers have inherent advantages in handling fragile and deformable objects e.g. fruits, food, biological tissues
However, even very deformable items like soft clays may require active force control to minimize deformation
Fig. 3: Experimental setup to gather data for fitting using random step changes in controls on a fixed cylinder (N = 58). Data was gathered at a sampling rate of 16 Hz.
Fig. 5: Contact jaw pressures from random perturbations of the grasper position () and control pressure (). The simulated response from the linear dynamics is shown in blue.
Fig. 6: Comparison of desired contact pressures and the simulated response with LQR. The stage cost corresponding to jaw 1’s pressure was given more weight to facilitate closer tracking of that trajectory.
Future Work
Fig. 2: Flow chart for controller development
A
B
C
Undeformed clay cube
After grasp
No force control
Observables:
Controls:
P1
P2
P3
x
y
x
y
. . .
x
y
Random step changes in controls
1
2
N
object
Soft graspers exhibit behaviors that are hard to analytically model e.g. non-linear material properties, hysteresis, deformable contact etc.
We use a data-driven approach to get the dynamics of the grasper so we can apply optimal control techniques.
Experimental Data
Fit dynamics
(MATLAB n4sid)
Design Controller:
LQR
Test controller on hardware
Goal: Track arbitrary contact pressure trajectories during grasping of rigid and deformable objects using optimal control techniques
Further refine the dynamics regression model:
  Parse the data and regression such that the dynamics model is fit solely to when the grasper experiences contact
  Perform cross validation on tracking error vs quantity of time delays embedded
  Cylinders of different sizes
  Materials of different rigidity (PLA and soft clay)
Try the LQR controller on hardware and compare the result to the simulation
Quantify deformation induced on deformable material with LQR controller and compare to existing neural-network open-loop controller [1]
References
[1] R. Sukhnandan et al., LNCS, 2023
16-745: Optimal Control and Reinforcement Learning
Discussion
The linear dynamics does not fully capture the experimental data
From the LQR simulation, Pc has a larger influence on the contact pressure compared to the x and y controls
  It may not be possible to individually track contact pressures on all three jaws